## Slide 1
Study of the effect of Drag correlations on Multiphase Eulerian-Eulerian Flow simulations
(Semester Long Internship at FOSSEE, IIT Bombay)
Project By:
M Siva Karthikeya
B.Tech Aerospace Engineering
Project Guide:
Prof. Janani Srree Muralidharan
Mechanical Dept, IIT Bombay
Project Coordinator:
Mr. Ashley Melvin
CFD Team, FOSSEE

## Slide 2: Contents
Problem Statement
Scientific Objectives
Timeline & Approach
Methodology
Drag Correlation Study
Results and Discussion
Inferences
Conclusion
Ongoing Work
References

## Slide 3: Problem Statement
“To identify the most reliable drag correlation for computational modelling of Dispersed Multiphase flows and see if a drag correlation performs equally well across two very different domains dealing with the same type of flow.”
Figure 1: Petroleum sector
Figure 2: Medical Sector

## Slide 4: Scientific Objectives
SCIENTIFIC OBJECTIVES | DESCRIPTION
Scientific Objective - I | To identify the most reliable drag correlation for computational modelling of Dispersed Multiphase flows.
Scientific Objective - II | To see if a drag correlation performs equally well across two very different and distinct domains dealing with the same type of flow.
Scientific Objective - III | To identify the miniscule parameters in a Multiphase study that can have significant impact on the end result.
Scientific Objective - IV | To understand the accuracy of Multiphase models in simulating a Fluidized Bed case by comparing with the experimental results obtained for the same.
Scientific Objective - V | To study the efficiency of Plasma extraction from a blood sample in a novel Backward facing step Microchannel design using a Single-phase and Multiphase analysis

## Slide 5: Timeline and Approach
Multiphase study of Novel Type Microchannel
Solid – Fluid Blood flow simulation – Syamlal O’Brien drag model
Week
12-Present
Multiphase study and Validation – Fluidized bed
Case Study project – Effect of Drag models on Fluidized bed
Week
6-11
Literature review
Single-phase Blood flow Validation study [4]
Week
1-5
Simulation of existing case studies in simpleFOAM solver
Domain creation for all 3 types of microchannel
Simulation of all 3 types using simpleFOAM solver and post-processing in Paraview
Multiphase modelling and analysis of Fluidized bed case study
Implementation of various drag correlations from literature
Post-processing and interpretation of results obtained
Fluid-Fluid simulations of Blood flow using multiphaseEulerFoam solver for Syamlal drag model.
Solid-Fluid simulations of Blood flow by implementing Kinetic Theory of Granular flow.

## Slide 6: Methodology – Geometry(1)
Figure 5: Type III Microchannel with dimensions
Figure 3: Type I Microchannel with dimensions
Figure 4: Type II Microchannel with dimensions

## Slide 7: Methodology – Geometry(2)
0.0762 m
y
x
Distributor
Gas Flow
Figure 6: Fluidized bed with marked lateral locations for particle velocity measurement

## Slide 8: Methodology – Mesh
Figure 7: Fluidized Bed Mesh
Table 1: Fluidized bed Mesh details
Details | Single-Phase | Multiphase
No.of Elements | 5,00,714 | 5076
Type | 3D | 2D
Cells | Hexahedral | Quadrilateral
Table 2: Microchannel Mesh details
Figure 8: Novel Type Microchannel Mesh
Details | Multiphase
Elements | 2806
Type | 2D
Cells | Quadrilateral

## Slide 9: Methodology – Boundary Conditions (1)
Boundary | U.air (m/s) | U. particles (m/s) | P_rgh | Theta
Inlet | interstitialInletVelocity (0 2.19 0) & alpha.air | fixedValue (0 0 0) | fixedFluxPressure | fixedValue
Outlet | pressureInletOutletVelocity phi.air | fixedValue (0 0 0) | prghPressure p = 101325 Pa | zeroGradient
Walls | noSlip | JohnsonJacksonParticleSlip | fixedFluxPressure | JohnsonJacksonParticleTheta
Table 3: Boundary conditions for Fluidized Bed case study

## Slide 10: Methodology – Boundary Conditions (2)
Boundary | /) | u (m/s)
Inlet | zeroGradient | 0.075
Outlet | fixedValue | zeroGradient
Walls | zeroGradient | noSlip
Boundary |  | u (m/s)
Inlet | zeroGradient | 0.075
Outlet | fixedValue | zeroGradient
Walls | zeroGradient | noSlip
Table 4: Boundary conditions for Single-Phase study of blood flow

## Slide 11: Solver Details
Multiphase study : twoPhaseEulerFoam
Eulerian–Eulerian multiphase solver.
Used for a system of 2 non-reacting compressible fluid phases, where one phase is always dispersed.
Uses the Finite Volume Method (FVM) to solve cell-centred and phase-averaged governing equations.
Each of the phases are treated as a continuum.
Single-Phase study : simpleFoam
Steady-state solver for incompressible, laminar, and turbulent flow.
Solver utilizes SIMPLE algorithm.
Finite volume method is used to solve the governing equations.
Multiphase study : twoPhaseEulerFoam
Fluidized Bed
Blood Flow in Microchannel

## Slide 12: Drag correlation study
Gidaspow-Ergun-Wen-Yu: This is a combination of the Ergun drag correlation applicable for dense systems and the Wen Yu correlation that can model a dilute flow where viscous forces are dominant, accurately.
Gidaspow-Schiller-Naumann: This drag correlation is capable of calculating the drag in a multi-particle system, unlike the Schiller-Naumann correlation which is restricted to a single particle system only.
Syamlal O’Brien: This drag correlation is based on the primary assumption that the Archimedes number remains the same for terminal settling velocity for both single and multi-particle systems.

## Slide 13: Results and Discussion
Figure 9: Contours of particle phase fraction ( at different timestamps
Figure 10: Velocity contour of Type III Microchannel at steady state

## Slide 14: Flow Ratio and Minimum Radius Comparison
Figure 11: Flow ratio comparison
Figure 12: Minimum Radius comparison

## Slide 15: Inferences (Single-Phase study)
Values of flow rate ratio and minimum radius obtained indicate that the results are in well agreement with those obtained in [4].
The slight deviation in the results is possibly due to the difference in mesh sizes/elements between computational domains of [4] and the ones used for this study (450k elements vs 500k elements).
The increase in flow ratio from Type I to Type II microchannel is an indication that the centrifugal effect due to the bent design aids in elevating the quantity of plasma that is being extracted from the side channel.
We can conclude from the results that the novel Type III design has the best flow rate ratio among others because of the combination of bent and converging inlet which aids is extraction of an increased amount of plasma from the side channel.

## Slide 16: Mean Eulerian Velocity Distribution ( = 2.19m/s)
Figure 13: Vertical velocity vs Lateral position plot for various drag correlations
Figure 14: Horizontal velocity vs Lateral position plot for various drag correlations

## Slide 17: Mean Eulerian Velocity Distribution ( = 3.28m/s)
Figure 15: Vertical velocity vs Lateral position plot for various drag correlations
Figure 16: Horizontal velocity vs Lateral position plot for various drag correlations

## Slide 18: Inferences (Fluidized Bed study)
Gidaspow-Schiller-Naumann correlation predicted the particle velocity distributions poorly for both the cases of gas velocity.
This can be attributed to the fact that it was primarily developed for packed bed applications where the gas velocity is relatively low, restricting the flow regime to a fixed bed.
Low values of specularity coefficient produce high particle velocities in the bed as there is less loss of tangential momentum to the walls [5].
Syamlal O’Brien’s drag correlation performed exceptionally well in replicating the experimental results[2] for both the gas velocities.
The reason for this realistic behaviour could be because of the consideration of the clustering effect [6] of particles in the model, unlike other correlations.

## Slide 20: Conclusion
Novel Type microchannel showed the best Flow rate ratio and Minimum radius values among other microchannel models. Thus, it is selected as the suitable model to conduct Multiphase study.
Syamlal O’Brien drag correlation outperformed others for both the cases of superficial gas velocity, 2.19 m/s and 3.28 m/s, by accurately predicting the Mean Eulerian particle velocity distributions at various lateral locations of the fluidized bed.
Multiphase Study of Blood flow provided useful insights about the inability of Syamlal model in simulating Fluid-Fluid flows.
Blood flow is considered as a solid-fluid dispersed flow with RBCs as the solid phase and Plasma as the fluid phase. Kinetic Theory of Granular Flow is being implemented for the Solid phase.

## Slide 21: Ongoing Study
Implemented the Blood flow (fluid-fluid) simulation for Syamlal O’Brien drag correlation using multiphaseEulerFoam solver. (Dispersed and Blended models)
Simulation crashes with a floating point error, which points to a mathematical error (division by 0 etc).
Arrived at a conclusion that Syamlal O’Brien cannot be applied to fluid-fluid systems.
Currently working on solid-fluid system case files of Blood flow with Syamlal drag correlation.

## Slide 22: References
[1] H, Enwald, E. Peirano, A-E Almstedt 'Eulerian Two-Phase Flow Theory Applied to Fluidization' Int. J. Multiphase Flow, Vol. 22, Suppl, pp. 21-66, 1996
[2] National Energy Technology Laboratory (NETL). (2013, May 30). Small Scale Challenge Problem I (2013). https://mfix.netl.doe.gov/experimentation/challenge-problems/small-scale-challenge-problem-i-2013/
[3] Ding, J. and Gidaspow, D. A bubbling fluidization model using kinetic theory of granular flow. AIChE Journal 36, 523-538, 1990
[4] Ashley Melvin, Janani Srree Murallidharan, Numerical Analysis of Plasma Extraction in a Backward facing Step Microchannel using OpenFOAM, FMFP2020–152, 2020.

## Slide 23: References
[5] Lungu, M., Wang, H., Wang, J., Yang, Y., & Chen, F. Two-Fluid Model Simulations of the National Energy Technology Laboratory Bubbling Fluidized Bed Challenge Problem. Industrial & Engineering Chemistry Research, 55(17), 5063–5077, 2016
[6] O'Brien, T. J. and Syamlal, M. Particle cluster effects in the numerical simulation of a circulating fluidized bed. 4th Int. Conf. on CFB, Somerset, USA, Preprint Volume, pp. 430—435, 199
[7] Johnson, P. C., & Jackson, R. Frictional–collisional constitutive relations for granular materials, with application to plane shearing. Journal of Fluid Mechanics, 176(-1), 67, 1987
[8] Khan, M. N., & Shamim, T. (2017). Influence of Specularity Coefficient on the Hydrodynamics and Bubble Statistics of an Annular Fluidized Bed Reactor. Energy Procedia, 105, 1998–2003.

## Slide 24: Thank You!